Sistema Remoto por Telefone
SDCC

---
Características SDCC
Open Source (GPL)
Cross Compiler
Otimizações
Portabilidade

---
Microcontroladores
Z80
MCS51
Pic16
Hc08
...

---
ATMEL AT89C52
#include <mcs51/at89x52.h>
__sfr __at 0x80 P0;
__sfr __at 0x81 SP;
__sfr __at 0x82 DPL;
__sfr __at 0x83 DPH;
__sfr __at 0x87 PCON;
__sfr __at 0x88 TCON;
__sfr __at 0x89 TMOD;
. . .
/* BIT addressable registers */
/* P0 */
__sbit __at 0x80 P0_0;
__sbit __at 0x81 P0_1;
__sbit __at 0x82 P0_2;
__sbit __at 0x83 P0_3;
...
#define IE0_VECTOR 0 /* 0x03 external interrupt 0 */
#define TF0_VECTOR 1 /* 0x0b timer 0 */
#define IE1_VECTOR 2 /* 0x13 external interrupt 1 */
#define TF1_VECTOR 3 /* 0x1b timer 1 */
#define SI0_VECTOR 4 /* 0x23 serial port 0 */
#define TF2_VECTOR 5 /* 0x2B timer 2 */
#define EX2_VECTOR 5 /* 0x2B external interrupt 2 */

---
Interrupções
Definindo uma função que é chamada com interrupação:
  - void <função>() __interrupt <interrupção>
Como funciona ?
Exemplo
  - void recebe_ligacao() __interrupt IE0_VECTOR {
    ...
    }

---
Áreas críticas
Definindo uma função que é chamada com interrupação:
  - void <função>() __critical
Como funciona ?
Exemplo
  - void cria_estados() __critical {
    ...
    }

---
Compilação
sdcc <arquivo.c>
Arquivos gerados:
  - arquivo.asm (Arquivo código em assembly)
  - arquivo.ihx (intel hex format)
  - arquivo.rel (Entrada para o Linker)

---
Mais informações
http://sdcc.sourceforge.org
http://sdcc.sourceforge.net/doc/sdccman.html/
http://www.maxim-ic.com/appnotes.cfm/appnote_number/3477